## Slide 1: Slides for Sagnac correction discussion
J. Wilkes, U. Washington
T2K Collab – Jan 21, 2014

## Slide 2: What is the Sagnac effect?
Sagnac effect refers to the phase shift observed in a light beam traveling in a closed path, when the path itself is rotating.
  In the Sagnac Interferometer shown below, light is sent in both directions around a loop
  If the loop rotates at constant w, the point of entry/exit (half-silvered mirror below) moves during the transit time of the light.
  The beam propagating against the direction of rotation has to cover less distance than the forward-propagating beam, and arrives back at the half-silvered mirror earlier.
  A corresponding phase shift is observed

## Slide 3: Sagnac for T2K neutrinos
Our “lab frame” (SK and J-PARC) is on the rotating Earth (ECEF = Earth-Centered, Earth-Fixed coordinate frame)
  We measure the neutrino flight path length L in the ECEF frame
  A neutrino takes about 1 millisec to travel the distance L
  Surface speed in an Earth-Centered Inertial (ECI) frame depends on latitude, and is about 750 m/s for T2K (path is almost due west)
  If a neutrino is emitted at J-PARC at t0 , SK has moved toward the neutrino about 37 cm by the time it arrives there
  This distance corresponds to about 1.23 ns of light-speed travel
    Our goal is to measure TOF to about 1 ns, so this is not negligible
  This is a purely macro geometric effect
    The SR effect (contraction of path length) for such a low relative speed between ECI and ECEF is negligible: 8 orders of magnitude smaller
t0
t0
t1
L
w

## Slide 4: TOF from GPS time
GPS system is designed to deliver an effectively “Newtonian” clock synchronized to the GPS master clock (atomic clock farm)
  GPS clocks anywhere on Earth “tick in unison”
    This means: if GPS clocks at Tokai and Mozumi emit a flash of light each second, an observer overhead, halfway between the two, sees the flashes simultaneously
  GPS receiver firmware takes into account GR and SR effects as well as Sagnac geometry effects: the appropriate Sagnac correction for the GPS clock in our receiver is built-in
  If the neutrino arrives at t1 , we are confident that the clock at J-PARC also read t1 “simultaneously”
  So, if the neutrino arrives with GPS-measured TOF Dt = t1 - t0 , we need to take into account the fact that its path length has been shorter than L by 37 cm
    One way to do this is to subtract 37 cm from the surveyed L value to compute the velocity of the neutrino
    Another way is to use L but add 1.23 ns to measured Dt